## Slide 1: Class Prerequisites and Goal
Before you start the class,
you should know Verilog
and the VCS simulator
GOAL: Acquire the skills to add SystemVerilog Assertions to your design, either from the Checker Library or written from scratch.
Notes: The goal of the 1 day SVA tutorial is to give users the skills necessary to add SystemVerilog Assertions to their design and verification environment. The training is also intended to give readers information on the SVA timing model, language, and syntax for writing custom assertions.

## Slide 2: Traditional Flow Has Multiple Entry Points For Introducing Bugs
Simulation
Testbench
Coverage
Formal analysis
Write checking code
Create monitors
Ad hoc definition/methods
Rewrite properties
Text and timing diagrams are not tool consumable
  Separate manual conversion for every tool
  Involves multiple persons, assumptions made
Specs
(text and timing diagrams)
Notes: You see, the issues comes from the fact that Specs are often written in text format.
MS word docs and timing diagrams are not machine readable, therefore they need to be separately translated into a form that can be used by each verification tool in your flow.
This manual translation can lead to many bugs. Ambiguities and assumption can be error prone and assumed capabilities can be left out of some verification steps.
Traditional flows are not very efficient.