## Slide 1: test
Black Box Design Planning
Gain Based RTL Synthesis
Design Planning and Prototyping
Block Implementation
Chip Integration
Chip Implementation
Notes: Here is a simple flow chart showing Magma’stop down hierarchical design flow. It starts in the early chip architecture phases and progresses all the way through final chip implementation with all steps using one data model, one executable, and the same engines for timing, extraction, optimization, placement, and routing. At each stage of the design process, the designer will use feedback provided by the tool to decide whether he should progress forward in the design flow or go back and modify input data including the design specification (RTL or netlist), the timing constraints, or the floorplan. As the design is getting proactively refined throughout this flow, the necessity to return to an early step will diminish as the design moves forward. Also, note that chip integration is not something you do at the end of the design process when all of the blocks are ready. In this flow, chip integration starts as soon as you know what blocks you’ll have in the design and create simple black box models for them.

## Slide 2: Test
Unbuffer
Convert to Supercells
Trim Gain
Low Effort Logic Optimization
Gain Report/
Timing OK?
Explore Time
Explore Plan
Explore Cell
Explore Clock
Netlist
Pad Placement / Power Mesh
Optional: Glassbox Generation
Top level
SDC
Volcano
(Blast RTL)
Notes: - Step 1 -
GAIN-BASED TIMING ANALYSIS
Unbuffer
Convert to super cells
Trimming
- Step 2 -
PROTOTYPE FLOORPLANNING
Chip size
IO planning
Macro placement
Cluster Placement
Partitioning/pin assignment
Time budgeting
Glassbox generation
- Step 3 -
PROTOTYPE PHYSICAL SYNTHESIS
Longwire Buffering
Global Routing
Sizing
Detailed Placement
- Step 4 -
PROTOTYPE CLOCK TREE SYNTHESIS
Clock routing
Low effort skew optimization